## Slide 1: Halloween Trick or Treat Bags
Visual Instructions

## Slide 2: Place right sides of fabric together

## Slide 3: Pin 3 sides leave the top of the bag unpinned

## Slide 4: Sew at a 1.5 cm seam allowance 3 sides
Multi-zigzag all 3 sides
Pivot at the corners for the Muti zig-zag
Finished sewing and multi zig-zag

## Slide 5: Handles
Fold handles good sides together and pin
Sew with a 1cm seam allowance the length of the handles
Repeat on second handle

## Slide 6: Handles continued – use the fast turner to turn the handle so the good side is facing out

## Slide 7: Press handles so the seam is “crisp”

## Slide 8: Measuring for placement of handles to the bag
Measure 2 inches from EACH side of the bag and make a mark
Repeat on the other side

## Slide 9: Attaching handles to bag
Pin the raw edge of the handle to the top of the bag beside where you marked the 2 inches.
Repeat on other side of bag with the other handle
Seam of the handle should face to the inside

## Slide 10: Attaching the handles
Baste stitch (5,A,4) each handle in place at a
1 cm seam allowance